## Slide 1: VIC DATA INPUTS AND OPTIONAL PROCESSES
Kel Markert
NASA-SERVIR Mekong Regional Associate
University of Alabama in Huntsville | Earth System Science Center
6 March 2017

## Slide 2: VIC MODEL INPUTS
The VIC model is complex requiring large amount of data in stored in multiple files
Much of the data can be acquired from remote sensing/GIS data sets
VIC Model
Global Parameters
Vegetation Parameters
Meteorological Forcing
Vegetation Library
Soil Parameters

## Slide 3: GLOBAL PARAMETER FILE
Main input file for VIC
Sets some model parameters and options
Points VIC to the locations of other input/output file
Sets parameters that govern the simulation
  Start/end dates
  Model modes
  Physical processes
Global parameter file documentation: http://vic.readthedocs.io/en/master/Documentation/Drivers/Classic/GlobalParam/

## Slide 4: SOIL PARAMETER FILE
Defines the spatial representation of the model
  Grid cell ID
  Latitude/longitude
Model links the rest of data inputs through soil file by using grid cell ID
Defines soil parameters at surface and each depth
Defines initial soil moisture conditions when no state file is used
Soil parameter file documentation: http://vic.readthedocs.io/en/master/Documentation/Drivers/Classic/SoilParam/
    Run value
    Grid cell ID
    Lat/Lon
    Soil parameters

## Slide 5: SOIL DATA
Soil information is poorly know
Harmonized World Soil Database (HWSD)
  30 arc-second (~1km) raster database
  Classified raster grid with database look-up information
  http://www.fao.org/soils-portal/soil-survey/soil-maps-and-databases/harmonized-world-soil-database-v12/en/
Contains over 15,000 different soil mapping units
  Has multiple soil parameters per mapping unit
  Used for soil pedotransfer functions
Accuracy and mapping information differs by region
  Example: Lower vs Upper Mekong
Region data differences

## Slide 6: VEGETATION PARAMETER FILE
Defines land cover types present and fractional areas for a grid cell
Also define rooting depths and rooting distributions for each land cover type
Optional parameter setting:
  Blowing snow
  LAI
  Vegetation cover
  Albedo
Vegetation parameter file documentation: http://vic.readthedocs.io/en/master/Documentation/Drivers/Classic/VegParam/
    Grid cell ID
    Number of vegetation classes
    Vegetation class
    Fractional cover
    Rooting depths
    Root distribution

## Slide 7: LAND COVER DATA AND PARAMETERIZATION
Can use whichever land cover dataset/classification best fits your needs
  Create vegetation parameter file
  Extract information for vegetation library
MODIS Combined Land Cover Product (MCD12Q1) IGBP classification
  Fairly accurate mapping at global scale
  Existing land cover parameterizations for land surface models
  https://lpdaac.usgs.gov/dataset_discovery/modis/modis_products_table/mcd12q1
Create your own land surface parameterization scheme or use existing
  NCAR NOAH LSM parameterizations
  http://www.ral.ucar.edu/research/land/technology/noahmp/HRLDAS-v3.6/VEGPARM.TBL

## Slide 8: VEGETATION LIBRARY FILE
Defines land parameterization for model
  Parameterization provided for each possible land cover class
  Library file referenced by vegetation parameter file
Vegetation library file documentation: http://vic.readthedocs.io/en/master/Documentation/Drivers/Classic/VegLib/

## Slide 9: LAND SURFACE PARAMETERIZATION
Use observed remote sensing datasets to create your own land surface parameterizations
  Need monthly climatology information for albedo and LAI parameters
MODIS LAI and albedo products (2000-present)
  LAI: https://lpdaac.usgs.gov/dataset_discovery/modis/modis_products_table/mod15a2
  Albedo: http://modis-atmos.gsfc.nasa.gov/ALBEDO/index.html
Can use remote sensing datasets for vegetation height, surface roughness, etc.
  Large errors with derived data
  Can lead to errors in model
Should you use observed remote sensing data or existing parameterization?

## Slide 10: ELEVATION BAND FILE
Not a required input
Used to partition grid cell into different elevation for more accurate orographic effects
Set maximum number of elevation band
  Each grid needs the maximum number of bands specified (fill non-existant bands with zeros)
Elevation band file documentation: http://vic.readthedocs.io/en/master/Documentation/Drivers/Classic/SnowBand/
    Grid cell ID
    Band percent coverage
    Average band elevation

## Slide 11: ELEVATION DATASETS
Plethora of DEM datasets available
  SRTM, GMTED, HydroSheds, NED, etc.
    http://www2.jpl.nasa.gov/srtm/
    https://lta.cr.usgs.gov/GMTED2010
    http://www.hydrosheds.org/
    https://lta.cr.usgs.gov/NED
STRM has relatively high accuracy, but also relatively high spatial resolution compared to model resolution
  Trade-offs between resolution and accuracy
Elevation data used to:
  Create snow bands file
  Prepare routing model inputs
  Parameterize soils inputs

## Slide 12: METEOROLOGICAL FORCING
VIC requires four meteorological variable inputs as a time series for each grid cell:
  Daily maximum temperature (°C)
  Daily minimum temperature (°C)
  Surface wind speed (m/s)
  Precipitation (mm)
Other meteorological inputs are supported:
  Sub-daily temperature(°C)
  Surface albedo (fraction)
  Atmospheric density (kg/m3)
  Downward short and longwave radiation (W/m2)
  etc.
Sub-daily meteorological data is needed for energy balance equations!

## Slide 13: METEOROLOGICAL FORCING (2 of 2)
Meteorological forcing data is used to drive the model processes
High degree of accuracy is needed for these datasets, otherwise model will not capture correct conditions
Meteorological forcing input data needs to be mapped to model grid cells
  Need to interpolate station data
Global datasets
  Temperature
    ERA-Interim, http://www.ecmwf.int/en/research/climate-reanalysis/era-interim
    MERRA-2, https://gmao.gsfc.nasa.gov/reanalysis/MERRA-2/
    CSFR, https://www.ncdc.noaa.gov/data-access/model-data/model-datasets/climate-forecast-system-version2-cfsv2#CFS
    Princeton dataset, http://hydrology.princeton.edu/data.pgf.php
    Reanalysis
  Precipitation
    Next slide…

## Slide 14: METEOROLOGICAL FORCING (1 of 2)
Global datasets (continued)
  Precipitation:
    CHIRPS, http://chg.geog.ucsb.edu/data/chirps/
    IMERG, https://disc.gsfc.nasa.gov/datareleases/imerg_data_release
    CMORPH, http://www.cpc.ncep.noaa.gov/products/janowiak/cmorph_description.html
    GPCC, https://www.esrl.noaa.gov/psd/data/gridded/data.gpcc.html
    Reanalysis
  Wind: Reanalysis
  Station data:
    GSOD, https://data.noaa.gov/dataset/global-surface-summary-of-the-day-gsod
    GHCN, https://www.ncdc.noaa.gov/data-access/land-based-station-data/land-based-datasets/global-historical-climatology-network-ghcn
  Typically lack spatial resolution but have required variables and temporal resolution

## Slide 15: VIC MODELING OPTIONS
VIC supports a wide variety of modeling applications
  Open source nature of model development
  You can contribute!
Can specify which model modes/components you would like to use for your own applications
  For example: Water balance mode vs full energy balance mode
  Most often needs additional data inputs
Example: http://hydro.washington.edu/forecast/monitor_west/

## Slide 16: SPATIAL DISTRIBUTION OF PRECIPITATION
Distributes precipitation throughout grid cell as a function of rain intensity
  Can account for orographic effects with small scale precipitation
  Parameterize using climatology
Fractional coverage is based on exponential relationship
Soil moisture is averaged for grid cell before a new storm occurs
Spatially distributing rain is parameterized within the snow bands file

## Slide 17: FROZEN SOIL SIMULATIONS
Important component in cold regions (high elevations or high latitudes)
Frozen soils can impede the infiltration of water content
Can alter spring soil moisture content and timing of streamflow
Has impact of the energy balance
  Energy balance is solved at each node within the soil and iterated for convergence
Image from Open Access VIC Documentation: http://vic.readthedocs.io/en/master/Overview/ModelOverview/

## Slide 18: LAKE AND WETLAND MODEL
Solves lake energy balance at different layers
  Incorporates lake ice coverage, more realistic representation of surface processed over lakes
  Takes into account water in/outflow
  Assumes ”one” lake per grid cell
Wetland model allows for season inundation of wetlands
  Better models the inter-annual water balance for wetland areas
  Channel/soil recharge depending on flux demand
Image from Open Access VIC Documentation: http://vic.readthedocs.io/en/master/Overview/ModelOverview/

## Slide 19: CARBON CYCLE MODEL
Allows for the simulation of vegetation photosynthesis and respiration
Plant phenology is not dynamic
  Based on land surface parameterization (monthly LAI climatology)
Vegetative biomass is not simulated
  Total carbon storage in plants
Calculates yearly Net Primary Productivity (NPP) based on vegetation type and meteorological conditions

## Slide 20: HYDROLOGIC STATE FILES
Users can save last model conditions (specifically soil moisture conditions) to file
Important if using the model for hydrologic forecasts
  Minimum model spin-up time is 1 year
Saves computation time
Model outputs are not consistent when using state files
  Small differences in soil moisture results between using and not using a state file

## Slide 21: THANK YOU
Kel Markert
kel.markert@nasa.gov